## Slide 1: Digital Signal Processing I
EEE 313
Dept. of EEE, BUBT

## Slide 2: Signal
Types by dimension:
1D: Audio, ECG
2D: Photograph
3D: Video
All natural signals are analog.
When an analog signal is sampled, quantized and coded, it becomes a digital signal.
“Stream of information that varies with some variables”
Continuous Signal: sin(Ωt)
Discrete Signal: sin(ωn)

## Slide 3: Sampling
x(t) = A cos(Ωt)
After sampling with Ts interval,
x(nTs) = A cos(ΩnTs) = A cos(2πFnTs) = A cos(2πnF/Fs) = A cos(2πfn)
Ω = Analog Angular Frequency (rad/second) = 2πF
F = Analog Frequency (cycle/second)
Fs = Sampling Frequency (sample/second) = 1 / Ts
f = Discrete Time Frequency (cycle/sample) = F / Fs
Example: f = 1/70 means “70 samples are collected in 1 cycle”.

## Slide 4: Nyquist's Sampling Theorem
For lossless reconstruction,
Fs ≥ 2F or, F / Fs ≤ 1 / 2 or, f ≤ 1 / 2
So, fmax can be 1 / 2.
Note: Smaller f is better. Because smaller f means: more samples are taken in each cycle.
“A bandlimited continuous-time signal can be perfectly reconstructed from its samples if the waveform is sampled over twice as fast as its highest frequency component.”

## Slide 5: Nyquist (continued)…
Fs = 1.1 F
Fs = 1.9 F
Fs = 2 F

## Slide 6: Periodicity
Previously, period was time. But here, period is sample.
Also, ω = 2πf = 2πk/N, and k is integer.
Note: f (= k/N) must be rational number.

## Slide 7: Question: Is “” a valid representation of discrete-time signal? Also find for “”.
Here, , which can not be a rational number.
So, NOT a valid representation.
Here, , which can not be a rational number (because π is irrational)
So, NOT a valid representation.

## Slide 8: Question: , where Hz and Hz. What is the minimum sampling frequency for lossless reconstruction? Find the expression of for 4000 Hz sampling frequency.
must be twice the maximum frequency component in .
So, it should be 6000 Hz.
Now,
So,

## Slide 9: continued…
Red: Blue:
Green:

## Slide 10: Time-Shifting of DT Sequence
Delay
y[n] = x[n - d], where d is integer.
Let, x[n] = [… 2 5 7 6 9 1 …]
y[n] = x[n-1]
y[-1] = x[-1-1] = x[-2] = 2
y[0] = x[0-1] = x[-1] = 5
y[1] = x[1-1] = x[0] = 7
y[2] = x[2-1] = x[1] = 6 and so on.
So, y[n] = [… 2 5 7 6 9 1 …]
Advance
y[n] = x[n + a], where a is integer.
Let, x[n] = [… 2 5 7 6 9 1 …]
y[n] = x[n+1]
y[-1] = x[-1+1] = x[0] = 7
y[0] = x[0+1] = x[1] = 6
y[1] = x[1+1] = x[2] = 9
y[2] = x[2+1] = x[3] = 1 and so on.
So, y[n] = [… 2 5 7 6 9 1 …]

## Slide 11: Basic Properties of Discrete-Time System
Memory
A system is memoryless if output depends only on present value.
Let, , where T{x[n]} means a transform in a system.
Now, , and so on.
It is memoryless.
Now let, .
Thus, , it depends on past value.
It needs memory.

## Slide 12: continued…
Now let, .
Thus, , it depends on future value.
It needs memory.
Question: x[n] = [9 6 5 1 4 0 7 0 3 …]; . Find y[-1], y[0], y[1], y[2], y[3]. Is this system memoryless?
y[-1] = x[-1] – x[0] = 1 – 4 = -3 y[0] = x[0] – x[1] = 4 – 0 = 4 y[1] = x[1] – x[2] = 0 – 7 = -7 y[2] = x[2] – x[3] = 7 – 0 = 7 y[3] = x[3] – x[4] = 0 – 3 = -3
The system depends on future values. So, not memoryless.

## Slide 13: continued…
(2) Linearity
A system is linear if it satisfies additivity & homogeneity of degree one.
(a) Additivity: For every pair of signal x1[n] and x2[n],
(b) Homogeneity of degree one: For every signal x[n] and scalar a,
Combining these two,
For example, let, .
Now,.
So, it’s non-linear.

## Slide 14: continued…
Additivity
Homogeneity

## Slide 15: continued…
Question: x1[n] = [ 2 0 4 6 …]; x2[n] = [ 1 3 2 7 …]. Using these sequences, show if linearity holds for the following system: y[n] = T{x[n]} = x2[n].
So,
The system is non-linear.

## Slide 16: continued…
Question: x1[n] = [ 2 0 4 6 …]; x2[n] = [ 1 3 2 7 …]. Using these sequences, show if linearity holds for the following system: y[n] = T{x[n]} = 2x[n].
So,
The system is linear.

## Slide 17: continued…
(3) Time-Invariance
A system is time-invariant if for all nd, the input with values produces output with values .
In other words:
(a) Get your output with no input delay, then delay the output. (b) Delay the input, then get output.
If both cases are matched, the system is time-invariant.

## Slide 18: continued…
Let,
x[n] = [… a b c d e f g h …]
y[n] = [… b d f h …] ; y[0]=x[0], y[-1]=x[-2], y[1]=x[2], y[2]=x[4]
y1[n] = y[n-1] = [… b d f h …] [output is delayed]; y1[0]=y[-1], y1[1]=y[0], y1[2]=y[1]
x[n-1] = [… a b c d e f g h …] [input is delayed]
y2[n] = [… a c e g …] [output for delayed input]
Here, .
So, it’s time-variant.

## Slide 19: continued…
Let,
x[n] = [… 2 4 3 8 6 4 2 1 4 9 5 9 7 …]
y[n] = [… 2 8 2 9 7 …] ; y[0]=x[0], y[-1]=x[-3], y[1]=x[3], y[2]=x[6]
y1[n] = y[n-1] = [… 2 8 2 9 7…] [output is delayed]; y1[-1]=y[-2], y1[0]=y[-1]
x[n-1] = [… 2 4 3 8 6 4 2 1 4 9 5 9 7 …] [input is delayed]
y2[n] = [… 3 4 4 9 …] [output for delayed input]
Here, .
So, it’s time-variant.

## Slide 20: continued…
Let,
x[n] = [… 4 1 2 5 0 1 …]
y[n] = [… 20 5 10 25 0 5 …]
y1[n] = y[n-1] = [… 20 5 10 25 0 5 …] [output is delayed]; y1[0]=y[-1], y1[1]=y[0]
x[n-1] = [… 4 1 2 5 0 1 …] [input is delayed]
y2[n] = [… 20 5 10 25 0 5 …] [output for delayed input]
Here, .
So, it’s time-invariant.

## Slide 21: Linear Time-Invariant (LTI) System
Unit impulse,
Now let,
Now,

## Slide 22: continued…
If linearity holds, then
And, for time-invariance, the impulse response,
So, for LTI system,

## Slide 23: Convolution Sum Formula
Using convolution sum, we can predict output for any kind of input without physically putting on the equipment.
Some properties of convolution:
Commutative:
Associative:
Distributive:

## Slide 24: (4) Stability
A system is stable if bounded input produces bounded output. [BIBO]
We know, for LTI system.
For stability of LTI system,
So, (Necessary & Sufficient condition)
This means, impulse response must be absolutely summable.

## Slide 25: Question: Find if the following systems are stable or not:
y[n] = x[n] – x[n+1]
If input is bounded, then difference between bounded values will also be bounded. So, the system is stable.
y[n] = x[n] + 7
If input is bounded, then addition of bounded values will also be bounded. So, the system is stable.
y[n] = log (x[n])
If 0 is found anywhere in the sequence x[n], then output becomes log(0) = – ∞. So, the system is unstable.
y[n] = n x[n]
Even if input is bounded, we don’t know the boundary of n. So, the system is unstable.

## Slide 26: (5) Causality
A system is causal if output depends on present and/or past input.
y[n] = 4x[n] System is causal.
y[n] = 2x[n-1] System is causal.
y[n] = 7x[n] + 5x[n-1] System is causal.
y[n] = 7x[n] + 5x[n+1] System is non-causal.
y[n] = 5x[n+1] System is anti-causal & non-causal.
Note: 1. All anti-causal systems are non-causal, but not the opposite. 2. All memoryless systems are causal. 3. Real-time system can not be non-causal.

## Slide 27: continued…
We know, for LTI system.
or,
For casual system, future values don’t exist.
So, h[-1] = h[-2] = h[-3] = … = 0
Simply, for any LTI system to be causal:
h[k] = 0, when k < 0

## Slide 28: Question: x[n]=[ 1 2 3 ], h[n]=[ 4 5 6 ]. Find the convolution.
y[0] = 4
y[1] = 5+8 = 13
y[2] = 6+10+12 = 28
y[3] = 12+15 = 27
y[4] = 18
So, y[n] = [ 4 13 28 27 18 ]
 |  | 1 | 2 | 3 |  |  | 
6 | 5 | 4 |  |  |  |  | 
 |  | 1 | 2 | 3 |  |  | 
 | 6 | 5 | 4 |  |  |  | 
 |  | 1 | 2 | 3 |  |  | 
 |  | 6 | 5 | 4 |  |  | 
 |  | 1 | 2 | 3 |  |  | 
 |  |  | 6 | 5 | 4 |  | 
 |  | 1 | 2 | 3 |  |  | 
 |  |  |  | 6 | 5 | 4 | 

## Slide 29: Question: x[n]=[ 1 2 3 4 5 ], h[n]=[ 4 5 6 ]. Find the convolution.
y[0] = 12+15+16 = 43
y[1] = 18+20+20 = 58
y[2] = 24+25 = 49
y[3] = 30
y[-1] = 6+10+12 = 28
y[-2] = 5+8 = 13
y[-3] = 4
So, y[n] = [4 13 28 43 58 49 30]
1 | 2 | 3 | 4 | 5 |  |  |  |  |  |  | 1 | 2 | 3 | 4 | 5
 | 6 | 5 | 4 |  |  |  |  |  |  |  | 6 | 5 | 4 |  | 
1 | 2 | 3 | 4 | 5 |  |  |  |  |  |  | 1 | 2 | 3 | 4 | 5
 |  | 6 | 5 | 4 |  |  |  |  |  | 6 | 5 | 4 |  |  | 
1 | 2 | 3 | 4 | 5 |  |  |  |  |  |  | 1 | 2 | 3 | 4 | 5
 |  |  | 6 | 5 | 4 |  |  |  | 6 | 5 | 4 |  |  |  | 
1 | 2 | 3 | 4 | 5 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 6 | 5 | 4 |  |  |  |  |  |  |  |  | 

## Slide 30: Convolution (graph)

## Slide 31: Quantization
“Process of mapping continuous infinite values to a smaller set of discrete finite values”

## Slide 32: Quantization by Rounding

## Slide 33: Quantization by Truncation

## Slide 34: Question: Quantize the sequence using integer rounding and truncation: x[n]= [ 7.4 2.3 6.5 5.7 9.2 -0.6 -1.9 0.5 -9.6 -2 -0.5 ]. Also find the error sequence.
Rounding: xq[n]= [ 7 2 7 6 9 -1 -2 1 -10 -2 -1 ]
Error: e[n] = [ -0.4 -0.3 0.5 0.3 -0.2 -0.4 -0.1 0.5 -0.4 0 -0.5 ]
Truncation: xq[n] = [ 7 2 6 5 9 0 -1 0 -9 -2 0 ]
  Error: e[n] = [ -0.4 -0.3 -0.5 -0.7 -0.2 0.6 0.9 -0.5 0.6 0 0.5 ]

## Slide 35: SQNR for Rounding
x[n] = Sample input
xq[n] = Quantized output
e[n] = Quantization error
Δ = Step size or Resolution
xmin = minimum of x[n]
xmax = maximum of x[n]
L = Number of level
Now,
where
SQNR: Signal to Quantization Noise Ratio

## Slide 36: continued…
If the signal is sinusoid, then xmax= A, xmin= - A.
For coding, if number of bits used is b, then [when b is higher]
And, for sinusoid,

## Slide 37: continued…
So,
log(ab) = log(a) + log(b)

## Slide 38: Question: An A/D converter uses 7-bit uniform rounding quantization for a sinusoidal signal. Find the SQNR(dB). If 8-bit was used, what would be the improvement in SQNR(dB)? If the sinusoid’s amplitude is 17, find resolution in both cases.
For 7-bit, SQNR(dB) = (1.76 + 6 x 7) dB = 43.76 dB
For 8-bit, SQNR(dB) = (1.76 + 6 x 8) dB = 49.76 dB So, the improvement is (49.76 – 43.76) dB, or, 6 dB
Resolution for 7-bit, Δ1 = (2 x 17) / (27) = 0.2656
Resolution for 8-bit, Δ2 = (2 x 17) / (28) = 0.1328

## Slide 39: Linear Constant-Coefficient Difference Equation (LCCDE)
Solution:
Homogeneous [zero-input], yh[n]
Particular [steady-state], yp[n]
Total solution = y[n] = yh[n] + yp[n]
y[n] = x[n] + 7 y[n-1] or, y[n] – 7 y[n-1] = x[n]

## Slide 40: Example: Find the homogeneous solution of a system described by the 1st-order difference equation: --------(i)
We know, [for order N]
Now, for eqn (i), [because it is 1st order]
Then, we substitute an assumed solution (for x[n]=0) in eqn (i).
So, the solution becomes -------(ii)
For n=0 (with x[n]=0), eqn (i) becomes
For n=0, eqn (ii) becomes

## Slide 41: continued…
So,
Then we substitute in eqn (ii),
Note: If the value of y[−1] is given, it must be included in the solution.
For y[−1] = 2,

## Slide 42: Example: Find the homogeneous solution of a system described by the 2nd-order difference equation: --------(i)
We know, [for order N]
Now, for eqn (i), [because it is 2nd order]
Then, we substitute an assumed solution in eqn (i).
So, the solution becomes -----(ii)
From eqn (i),

## Slide 43: continued…
From eqn (ii),
-----(iii)
-----(iv)
After solving eqn (iii) and (iv),
for

## Slide 44: Correlation
Crosscorrelation:
Autocorrelation:
“Measure of similarity between signals”
Use: radar, sonar, GPS etc.

## Slide 45: Convolution vs Crosscorrelation vs Autocorrelation
rfg
rgf
rff
rgg

## Slide 46: Question: Find rxy[n] and ryx[n] for the following: x[n]=[ 7 4 6 1 ], y[n]=[ 1 0 1 9 ].
rxy[0] = 0+4+54 = 58
rxy[1] = 7+0+6+9 = 22
rxy[2] = 4+0+1 = 5
rxy[3] = 6+0 = 6
rxy[4] = 1
rxy[-1] = 7+36 = 43
rxy[-2] = 63
So, rxy[n] = [ 63 43 58 22 5 6 1 ]
And, ryx[n] = [ 1 6 5 22 58 43 63 ]
 | 7 | 4 | 6 | 1 |  |  |  |  |  |  |  | 7 | 4 | 6 | 1
1 | 0 | 1 | 9 |  |  |  |  |  |  | 1 | 0 | 1 | 9 |  | 
 | 7 | 4 | 6 | 1 |  |  |  |  |  |  |  | 7 | 4 | 6 | 1
 | 1 | 0 | 1 | 9 |  |  |  |  | 1 | 0 | 1 | 9 |  |  | 
 | 7 | 4 | 6 | 1 |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 0 | 1 | 9 |  |  |  |  |  |  |  |  |  | 
 | 7 | 4 | 6 | 1 |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 1 | 0 | 1 | 9 |  |  |  |  |  |  |  |  | 
 | 7 | 4 | 6 | 1 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 1 | 0 | 1 | 9 |  |  |  |  |  |  |  | 

## Slide 47: Question: Find autocorrelation for the following: x[n]=[ 7 4 6 ]
rxx[0] = 49+16+36 = 101
rxx[1] = 28+24 = 52
rxx[2] = 42
rxx[-1] = 28+24 = 52
rxx[-2] = 42
So, rxx[n] = [ 42 52 101 52 42 ]
 |  | 7 | 4 | 6 |  | 
 |  | 7 | 4 | 6 |  | 
 |  | 7 | 4 | 6 |  | 
 |  |  | 7 | 4 | 6 | 
 |  | 7 | 4 | 6 |  | 
 |  |  |  | 7 | 4 | 6
 |  | 7 | 4 | 6 |  | 
 | 7 | 4 | 6 |  |  | 
 |  | 7 | 4 | 6 |  | 
7 | 4 | 6 |  |  |  | 

## Slide 48: continued…
Normalized Correlation Sequence
For example, if
then

## Slide 49: Discrete Time Fourier Transform (DTFT)
is a continuous function of ω, where ω = ΩTs.
is periodic with period of 2π.
To convert to x[n], inverse DTFT (IDTFT) is applied:
where k is any integer

## Slide 50: continued…
Discrete & Aperiodic
Continuous & Periodic

## Slide 51: continued…
Spectra
Existence of DTFT
Sufficient condition:
x[n] must be absolutely summable.
Then, DTFT converges to a finite result for all ω.
is generally complex.
Magnitude spectrum:
Phase spectrum:
Note: Both are continuous & periodic.

## Slide 52: continued…
Unit Impulse
Unit Step
δ[n] = [ … 0 0 0 0 1 0 0 0 0 … ]
u[n] = [ … 0 0 0 0 1 1 1 1 1 … ]

## Slide 53: Question: Find the DTFT of x[n] = u[n] – u[n-3]
u[n] = [… 0 0 0 0 0 1 1 1 1 1 1 1 1 …]
u[n-3] = [… 0 0 0 0 0 0 0 0 1 1 1 1 1 …]
x[n] = [… 0 0 0 0 0 1 1 1 0 0 0 0 0 …]
We know,

## Slide 54: Question: Find the DTFT of
We know,
But, u[n] = 0 when n < 0.
So,
This is a convergent geometric series (because the |ratio| is < 1)
[ using formula ]
u[n]

## Slide 55: Question: Find the IDTFT of
We know,
[ We know, ]

## Slide 56: continued…

## Slide 57: Some Properties of DTFT
Linearity
Time Delay
Frequency Shift
Convolution
Differentiation

## Slide 58: continued…
Time Reversal
Conjugation
Modulation
Multiplication
Parseval’s Theorem

## Slide 59: Discrete Fourier Transform (DFT)
We take N equidistant samples in the interval with spacing
where k = 0,1,2,…,N–1
Recall the DTFT of x[n],
Let’s sample X(ω) periodically in frequency at a spacing of .
Since X(ω) is periodic with period 2π, only samples in the fundamental frequency range are necessary.

## Slide 60: continued…
But, the equally spaced frequency samples do not uniquely represent the original sequence x[n] when x[n] has infinite duration.
Instead, the frequency samples correspond to a periodic sequence of period N, that is an aliased version of x[n].
So, a finite-duration sequence x[n] of length L has a DTFT:
After equidistant sampling of X(ω) for N ≥ L,
where k = 0,1,2,…,N–1
The N-point inverse DFT (IDFT):
where n = 0,1,2,…,N–1

## Slide 61: continued…
Let’s see the DTFT and DFT of

## Slide 62: Example: Find the 4-point DFT of x[n]=[ 2 1 7 5 ]
where k = 0, 1, 2, 3
Magnitude,
Angle,

## Slide 63: z-Transform
Example: Determine the z-transforms of the following finite-duration signals:
x1[n]=[ 9 2 4 6 3 1 ] X1(z)=9z2+2z+4+6z–1+3z–2+z–3, ROC: entire z-plane except z=0 and z=∞
x2[n]=[ 1 0 7 9 5 ] X2(z)=1+7z–2+9z–3+5z–4, ROC: entire z-plane except z=0
where z is a complex variable.
The Region of Convergence (ROC) of X(z) is the set of values of z for which X(z) attains a finite value.

## Slide 64: More example: Determine the z-transforms of the following finite-duration signals:
x3[n]=δ[n] X3(z)=1 ; ROC: entire z-plane
x4[n]=δ[n–6] X4(z)=z–6 ; ROC: entire z-plane except
x5[n]=δ[n+7] X5(z)=z7 ; ROC: entire z-plane except
x6[n]=[ 4 6 0 7 ] X6(z)=4z3+6z2+7; ROC: entire z-plane except

## Slide 65: Example: Determine the z-transform of the signal:
We get,
Thus,
Recall for infinite geometric series, , where
So,

## Slide 66: Existence of X(z)
Let, , where , and
In the ROC of X(z),
So, is finite if is absolutely summable.

## Slide 67: continued…
ROC for 1st sum consists of all points inside a circle of radius
ROC for 2nd sum consists of all points outside a circle of radius
Thus, X(z) exists if
If , there is no common ROC, and X(z) doesn’t exist.

## Slide 68: continued…
Recall the example:
Similarly,
where can be real or complex.

## Slide 69: Example: Determine the z-transform of the signal:
We get,
Thus,
Recall for infinite geometric series, , where
So,

## Slide 70: continued…
Recall the previous example:
Similarly,
where can be real or complex.

## Slide 71: Example: Determine the z-transform of the signal:
For the 1st term,
For the 2nd term,
If , two ROC don’t overlap. So, X(z) doesn’t exist.
If , the ROC is ring-shaped. X(z) exists.
For 2nd case,

## Slide 72: ROC Characteristic
Finite-Duration Signal
Infinite-Duration Signal
(Causal)
(Anti-Causal)
(Two-Sided)

## Slide 73: Some Properties of z-Transform
Linearity:
Example: Find the z-transform for
We get,

## Slide 74: continued…
Time-Shifting:
Example: Using time-shifting, find z-transform for y1[n]=x[n+3] and y2[n]=x[n-2]; where x[n]=[ 2 0 5 4 6 3 ].
We get,

## Slide 75: continued…
Scaling: If
Then
Time Reversal: If
Then
Example: Determine the z-transform for x[n]=u[-n].
Recall that,

## Slide 76: continued…
Differentiation:
Example: Determine the z-transform for
We recall,

## Slide 77: continued…
Convolution:
Example: Using convolution property of z-transform, find , where x1=[ 5 0 7 ], x2=[ 2 4 ]

## Slide 78: Poles & Zeros for Rational X(z)
The zeros of X(z) are the values of z for which
The poles of X(z) are the values of z for which
Note:
ROC of X(z) should not contain any poles.
If N > M, then X(z) has (N–M) zeros at origin.
If M > N, then X(z) has (M–N) poles at origin.
Poles or zeros may also occur at

## Slide 79: Example: Determine the pole-zero plot for the signal:
We recall,
X(z) has one zero at z=0
X(z) has one pole at z=4

## Slide 80: Time-Domain Behavior with Pole Location “Causal Sequence ”
Single Real Pole (Positive)
Single Real Pole (Negative)

## Slide 81: Time-Domain Behavior with Pole Location “Causal Sequence ”
Double Real Pole (Positive)
Double Real Pole (Negative)

## Slide 82: continued…
Causal real signals with simple real poles or simple complex conjugate pairs of poles, which are inside or on the unit circle, are always bounded in amplitude.
Time behavior of a signal depends strongly on the location of its poles relative to the unit circle.
Zeros also affect the behavior of a signal but not as strongly as poles.

## Slide 83: Some Common z-Transform Pairs
x[n] | X(z) | ROC
 | 1 | Entire z-plane
x[n] | X(z) | ROC
 | 1 | Entire z-plane

## Slide 84: Inverse z-Transform
where C is a counterclockwise closed path encircling the origin and entirely in ROC.
Methods:
Direct evaluation by contour integration
Expansion into a series of terms, in the variables
Partial-fraction expansion and table lookup

## Slide 85: Example: Find the inverse z-transform for
We get,
Putting , we get
Putting , we get

## Slide 86: continued…
----------------(i)
So, x[n] is causal, and both terms in eqn (i) are causal terms.
What if ?
So, x[n] is anti-causal, and both terms in eqn (i) are anti-causal terms.

## Slide 87: continued…
----------------(i)
What if ?
So, x[n] is two-sided, and one term in eqn (i) is causal, another is anti-causal.
For ROC to exist (overlap):
provides causal part.
provides anti-causal part.

## Slide 88: Example: Find the inverse z-transform for
We get,
After solving,

## Slide 89: Example: Find the inverse z-transform for
We get,
After solving,
Formula: where and
Note: Here,

## Slide 90: System Function
H(z) represents the z-domain characterization of a system, whereas h[n] is the corresponding time-domain characterization of the system.
Example: Determine the system function and the impulse response of the causal system described by the difference equation:
Computing the z-transform of this difference equation,
Note: This system has pole at and zero at origin.

## Slide 91: Example: An LTI system has . Find the system’s unit step response.
We get,
And,

## Slide 92: Example: Compute the step response of a causal LTI system with zero at 1, pole at 3, and H(0) = 4. Also find the LCCDE.
Let,
And,

## Slide 93: Causality & Stability with z-Transform
An LTI system is causal if and only if the ROC of H(z) is the exterior of a circle of radius , including the point .
An LTI system is BIBO stable if and only if the ROC of H(z) includes the unit circle.
A causal LTI system is BIBO stable if and only if all the poles of H(z) are inside the unit circle.

## Slide 94: Example: An LTI system is characterized by the following system function: System is non-causal. Specify ROC of H(z). Determine h[n]. Find stability.
After partial-fraction expansion, we get:
Since the system is non-causal (given),
ROC contains “unit circle”, so the system is stable.

## Slide 95
What if the system is causal?
ROC doesn’t contain “unit circle”, so the system is unstable.
What if the system is anti-causal?
ROC doesn’t contain “unit circle”, so the system is unstable.
continued…

## Slide 96: Pole-Zero Cancellation
When a z-transform has a pole that is at the same location as a zero, the pole is cancelled by the zero.
H(z) itself → order of the system reduced by one.
Product of H(z) and X(z) → pole of the system suppressed by zero in x[n], or vice versa.
By proper selection of the zeros of x[n], it is possible to suppress one or more system modes in the response of the system.
By proper selection of the zeros of H(z), it is possible to suppress one or more modes of x[n] from the response of the system.

## Slide 97: Example: Find h[n] for a causal system is described by the following LCCDE:
We get,
Applying z-transform,

## Slide 98: Example: A causal LTI system is described by: Find the input signal that will cancel the nearest pole to the origin. Also find system response for that input.
This system has two real poles at and
System
The nearest pole is at (to be cancelled).
So, X(z) must be
Now,

## Slide 99: continued…
What if you want to cancel the farthest pole from the origin?
The farthest pole is at (to be cancelled).
So, X(z) must be
Now,

## Slide 100: Example: A cell phone signal is distorted by multipath reflections off of city buildings. What your cell phone receives is not but , where . Can you find a filter that recovers from ?
We need to compute the inverse filter that can undo the effect of .
We want , which implies .

## Slide 101: continued…

## Slide 102: Digital Filter
Analog vs Digital
Analog filters are cheap, fast, and have a large dynamic range.
Digital filters are vastly superior in the level of performance.
Digital Filter Type
FIR Filter: has Finite Impulse Response [carried out by convolution]
IIR Filter: has Infinite Impulse Response [carried out by recursion]
Use:
Signal separation (e.g. EKG contaminated with noise)
Signal restoration (e.g. image captured with shaky camera)

## Slide 103: Filter Parameters
Every linear filter has
impulse response
step response
frequency response
Some info about dB:
Every 20 dB means that the amplitude has changed by a factor of 10.
-3 dB means that the amplitude is reduced to 0.707, and the power is reduced to 0.5.

## Slide 104: Information is Represented in Signals
Step response describes how information represented in the time domain is being modified by the system.
Frequency response shows how information represented in the frequency domain is being changed.
Good performance in the time domain results in poor performance in the frequency domain, and vice versa.
Example:
Filter for noise removal from an EKG: step response is the important parameter, and frequency response is of little concern.
Filter for a hearing aid: frequency response is all important, while step response doesn't matter.

## Slide 105: Time Domain Parameters of Digital Filter
Better:
Fast step response
No overshoot
Linear Phase

## Slide 106: Frequency Domain Parameters of Digital Filter
Better:
Fast roll-off
Flat passband
Good stopband attenuation

## Slide 107: Low-Pass Filter to High-Pass Filter

## Slide 108: Band-Pass & Band-Reject Filter from LPF & HPF

## Slide 109: Moving Average Filter
For example, a 5-point MA filter:
A 5-point filter has the filter kernel:
That is, MA filter is a convolution of the input signal with a rectangular pulse having an area of unity.
Remember: MA filter is an FIR filter.
Alternatively,

## Slide 110: continued…
The amount of noise reduction is equal to the square-root of the number of points in the average.
For example, a 100 point moving average filter reduces the noise by a factor of 10.

## Slide 111: Frequency Response of MA Filter
MA is an exceptionally good smoothing filter.
But, MA is an exceptionally bad low-pass filter.
Frequency response of an M-point MA filter:

## Slide 112: Windowed-Sinc Filter
While this infinite length (in time domain) is not a problem for mathematics, it is a show stopper for computers.
Now there is excessive ripple in the passband and poor attenuation in the stopband.
Increasing the length of the filter kernel does not reduce these problems.

## Slide 113: continued…
Windowing comes to the rescue!
Multiplying the truncated-sinc (c), by the Blackman or Hamming window (e), results in the windowed-sinc filter kernel shown in (f).
The passband is now flat, and the stopband attenuation is so good it cannot be seen in this graph.

## Slide 114: Window: Hamming vs Blackman
Hamming Window:
Blackman Window:
Comparison:
Hamming has about a 20% faster roll-off than Blackman.
Blackman has a better stopband attenuation ( dB) than Hamming ( dB).
Blackman has a passband ripple of about 0.02%, while Hamming is typically 0.2%.
Conclusion:
In general, Blackman should be your first choice; a slow roll-off is easier to handle than poor stopband attenuation.

## Slide 115: Designing the Windowed-Sinc Filter
Parameters:
Cutoff frequency,
Length of the filter kernel,
Value for sets the roll-off:
Both and are expressed as fraction of the sampling rate. Thus, they must be between and .
is measured at the one-half amplitude point.
M=60

## Slide 116: continued…
Filter Kernel: (Blackman LPF)
for
is chosen to provide unity gain at zero frequency (normalizing coefficient).
must be an even integer.

## Slide 117: Example: EEG pattern containing alpha rhythm occurs between 7 and 12 Hz, and beta rhythm occurs between 17 and 20 Hz. Design a Blackman LPF that can separate alpha from beta rhythms. The EEG signal was digitized at a sampling rate of 100 sample/second. Set your transition bandwidth at 4 Hz.
Let, Hz of sampling rate.
Given, Hz of sampling rate.
for

## Slide 118: Kaiser Window
is the length of the window.
is the shape parameter.
Large values of result in reduced ripple.

## Slide 119: continued…
where is the 0th-order modified Bessel function of the 1st kind, that can be easily generated using:
A Kaiser Window is nearly optimum in the sense of having the most energy in its main-lobe for a given side-lobe amplitude.
James Frederick Kaiser

## Slide 120: Example: Design an FIR LPF using Kaiser window according to the following specifications
Solve:

## Slide 121: continued…
where

## Slide 122: IIR (Recursive) Filter
are called Recursion Coefficients.
IIR filters execute very rapidly, but have less performance and flexibility than other digital filters.
In theory, recursive filter convolves the input signal with a very long filter kernel; although only a few coefficients are involved.
3-stage Recursive Filter

## Slide 123: Single Pole Recursive Filter
LPF
HPF
Proper coefficient selection can also make the digital recursive filter mimic an analog RC HPF or LPF.

## Slide 124: continued…
Coefficient Selection: (Single Pole IIR Filter)
LPF:
HPF:
Physically, is the amount of decay between adjacent samples.
For example, means that the value of each sample in the output signal is the value of the sample before it.
The higher the value of , the slower the decay.
, where dB cutoff frequency.

## Slide 125: continued…
Single Pole Recursive Filter in action:
(for LPF), (for HPF)
Remember: Single Pole Recursive Filter performs well in the time-domain, and poorly in the frequency-domain. Performance at higher (with respect to sampling rate) is terrible!

## Slide 126: Special: 4-stage Recursive LPF
[comparable to the Blackman, but faster]
Coefficient Selection:
where

## Slide 127: Narrow-band Filters
Band-Pass Filter
Band-Reject Filter
where ;
center frequency
bandwidth measured at 0.707 amplitude
[both expressed as fraction of sampling frequency]

## Slide 128: Phase Response
What is so wrong with nonlinear phase? Many applications cannot tolerate the left and right edges looking different. This can be misinterpreted as a feature (terrible)!!!
of recursive filter is not symmetrical between left and right, therefore has a nonlinear phase.